Composites Creel Specification

The Cygnet Texkimp Composites creels are designed for the unwinding of high performance multifilament packages into a large range of low and high speed downstream processes. Each creel is specifically designed and configured to accommodate the individual fibre, process and site requirements.

| Process | Low speed – Weaving, Pre-preg, Tow-preg, Pultrusion, Impregnation, Coating, Laminating, Warp Knitting High speed – Beaming, warping and section warping. |
| --- | --- |
| Materials / Applications | Carbon Fibre, Aramid, Glass, others |
| Typical Speed | Low speed - Standard CF - Up to 25m/min High speed - Upgraded CF - Up to 200m/min |
| Unwinding | Type : Unrolling Yarn Path : Vertical or Horizontal |
| Typical Arrangement | Bespoke to accommodate each projects requirements. Customisable, trolley or fixed design |
| Packages - Standard CF range | Type : Precision cross-wound packages, on parallel sided tubes Max. Traverse : 250mm (10”) Max. Dia : Up to 310mm (12”) Max. Weight : Up to 12kgs (26lbs) |
| Packages - Upgraded CF range | Type : Precision cross-wound packages, on parallel sided tubes Max. Traverse : 350mm (14”) Max. Dia : Up to 450mm (16”) Max. Weight : Up to 40kgs (90lbs) |
| Features Available | Bespoke layouts to suite project requirements. Precise calibration of each running position at commissioning stage. All tows kept separate from package to process. Centrally adjustable tension system or Automated Tension Control System based on diameter or load to ensure constant tension control from full to empty packages. Low cost simple gravity weighted tension system. Interchangeable package holders or adaptors for different sizes. Standard or needle bearings for friction / tension requirements of application. Pneumatic quick stop breaking linked to downstream processes. Quick thread or closed eyelet guide systems. Fixed and variable-width condenser boards. End break detection systems. |
| Specification can be varied to suit any requirement |

# Optional extras:

# End Break Detection System - Beamer Type

End Break Detection System – Dropper Type

Fixed and Variable Condenser Boards and Combs

Splicers, Splice Tables, Splice Ovens